## Slide 1: 198:211 Computer Architecture
Abhishek Bhattacharjee
Topics:
  Integer Arithmetic

## Slide 2: Review

## Slide 3: Two’s Complement
000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
0 | 1 | 2 | 3 | -4 | -3 | -2 | -1
One’s complement plus one
  Most significant bit still gives the “sign”
  Trick: copy all ‘0’ bits from LSB till first ‘1’ bit. Copy ‘1’ bit, then flip all remaining bits till MSB.
Advantages:
  Only 1 zero
  Most convenient for arithmetic computations
Used in almost all computers today

## Slide 4: IEEE floating point standard
Most computers follow IEEE 754 standard
Single precision (32 bits)
Double precision (64 bits)
Extended precision (80 bits)
S
Fraction
Exponent

## Slide 5: Floating point in C
32 bits single precision (type float)
  1 bit for sign, 8 bits for exponent, 23 bits for mantissa
    Sign bit: 1 = negative numbers, 0 = positive numbers
    Exponent is power of 2
  Have 2 zero’s
  Range is approximately -1038 to 1038
64 bits double precision (type double)
  1 bit for sign, 11 bits for exponent, 52 bits for mantissa
  Majority of new bits for mantissa  higher precision
  Range is -10308 to +10308

## Slide 6: Numerical Values
Three different cases:
  Normalized values
    exponent field ≠ 0 and exponent field ≠ 2k-1 (all 1’s)
    exponent = binary value – Bias
      Bias = 2k-1-1 (e.g., 127 for float)
    mantissa = 1.(mantissa field)
    Ex: (sign: 0, exp: 1, mantissa: 1) would give 0b1.1x2-126
  Denormalized values
    exponent field = 0
    exponent = 1 – Bias (e.g., -126 for float)
    Mantissa = mantissa field (no leading 1)
    Ex: (sign: 0, exp: 0, mantissa: 10) would give 0b10x2-126
  Special values: represent +∞, -∞, and NaN

## Slide 7: Decimal to IEEE Floating Point
5.625
In binary
101.101  1.01101 x 22
Exponent field has value 2
  add 127 to get 129
Exponent is 10000001
Mantissa is 01101
Sign bit is 0
0 10000001 0110100000000000000000

## Slide 8: Computer Arithmetic
Today, we are going to revisit our mathematic 101
Why?
  Finite number of bits
  Number representation (e.g., two’s complement)
  Develop algorithms easy to implement in hardware

## Slide 9: Unsigned Addition and Subtraction
6 0110
- 5 0101
------------
1 0001
5 0101
+ 6 0110
--------------
11 1011
6 0110
- 5 1011
------------
1 0001

## Slide 10: Overflow
What happens to the following addition if each number is represented by only 4 bits?
Adding two n bits numbers may result in an n+1 bit number
No space to hold extra bit  modulo arithmetic
  x + y is really (x + y) mod 2n, where n = number of bits
  (8 + 10) mod 24 = 2
8 1000
+ 10 1010
------------
18 10010
8 1000
+ 10 1010
------------
2 10010

## Slide 11: Overflow
An overflow occurs when the result cannot fit within the size limit of the data type
When executing C programs, overflows are not signaled as errors!
Programmer must figure it out
When two unsigned numbers x, y are added
Overflow has occurred if
  x+y < x or x+y < y

## Slide 12: 2’s Complement Addition & Subtraction
Addition = binary addition, ignore carry out
Subtraction = invert subtrahend and add
4 – 2 = 4 + -2
-7 1001
+ 5 0101
----------
-2 1110
-5 1011
+ -2 1110
------------
-7 11001
4 0100
+ -2 1110
------------
2 0010

## Slide 13: 2’s Complement Addition
Why does it work?
  Adding 2 positive numbers: obvious
  Adding positive and negative number?
    |pos number| > |neg number|
      Will wrap around  0 MSB
    |neg number| > |pos number|
      Will not wrap  1 MSB
  Adding 2 negative numbers just like adding two positive numbers
    Will always wrap  1 MSB is preserved
2+(-1)=1
-4 1 00
-3 1 01
-2 1 10
-1 1 11
0 0 00
1 0 01
2 0 10
3 0 11

## Slide 14: 2’s Complement Overflow
What happens when overflow occurs with 2’s complement?
  Need one extra bit so sign bit will be wrong
  How to detect?
    Adding 2 positive numbers  negative result
    Adding 2 negative numbers  positive result
6 0110
+ 5 0101
-----------
-5 1011
-6 1010
+ -6 1010
------------
4 0100

## Slide 15: Unsigned Multiply
How can we compute n x m?
Not very efficient …

## Slide 16: Unsigned Multiplication
Notice anything about the binary form?
54
x 67
----
378
324
----
3618
1011
x 101
------
1011
0000
1011
------
110111

## Slide 17: Algorithm
1011
x 101
------
1011
0000
1011
------
110111
(multiplicand x 1) shift left 0
(multiplicand x 0) shift left 1
(multiplicand x 1) shift left 2

## Slide 18: Algorithm
result = 0
If LSB of multiplier = 1, add multiplicand to result else, add 0 to result
Shift multiplicand left by 1 bit (fill LSB with 0)
Shift multiplier right by 1 bit (fill MSB with 0)
If multiplier > 0, go to 1
Stop
We only need to know how to add and shift in order to multiply

## Slide 19: Overflow
The result of multiplying two n-bits long numbers can be up to 2n-bits long
What to do with the extra bits?
  Discard n most significant bits  modulo arithmetic
  Some processors leave results in two registers so programmer can have entire result if desired

## Slide 20: Signed Multiplication
When multiplying two n-bits signed number, if you just want the n least significant bits of the result, then a very slightly modified algorithm works
  Book develops a mathematical proof
If want all 2n bits of result, then what?
  Convert both multiplicand and multiplier to positive numbers
  Multiply
  Apply correct sign
    Same signs before: positive
    Different signs before: negative
111
X 111
------
111
111
111
------
110001

## Slide 21: Algorithm
result = 0
If LSB of multiplier = 1, add multiplicand to result else, add 0 to result
Shift multiplicand left by 1 bit (fill LSB with 0)
Shift multiplier right by 1 bit (fill MSB with sign bit)
If multiplier > 0, go to 1
Stop

## Slide 22: Sign extension
Signed integer | 4-bit representation | 8-bit representation | 16-bit representation
+1 | 0001 | 00000001 | 0000000000000001
-1 | 1111 | 11111111 | 1111111111111111

## Slide 23: Unsigned Division
How can we compute n / m?
  Count how many times we can subtract n from m until the remainder r is less than m
  Call this count q
Again, not very efficient …

## Slide 24: Unsigned Division
53 ÷ 7 = 7 rem 4
 |  |  |  |  |  |  | 0 | 1 | 1 | 1 |  | 
Divisor q=0 |  | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 |  | Dividend
q=1 |  |  |  |  | 0 | 1 | 1 | 1 |  |  |  | 
 |  |  |  |  | 0 | 1 | 1 | 0 | 0 |  |  | 
q=1 |  |  |  |  | 0 | 0 | 1 | 1 | 1 |  |  | 
q=1 |  |  |  |  | 0 | 0 | 1 | 0 | 1 | 1 |  | 
 |  |  |  |  | 0 | 0 | 0 | 1 | 1 | 1 |  | 
 |  |  |  |  |  |  | 0 | 1 | 0 | 0 |  | Remainder

## Slide 25: Algorithm
Shift divisor left, filling LSB with 0, until same number of bits as dividend
quotient = 0, remainder = dividend
If remainder < original divisor, stop
If remainder < divisor, shift quotient left, fill LSB with 0
If remainder ≥ divisor, shift quotient left, fill LSB with 1
  remainder = remainder – divisor
Shift divisor right, fill MSB with 0
Go to 3
Only need subtract and shift to implement division

## Slide 26: Signed Division?
Change any negative number to positive number
Perform division
Compute signs of quotient and remainder
Negate quotient and/or remainder if necessary

## Slide 27: What About Floating Point?
Addition and Subtraction
  Scientific form: have to align “.” so exponents are the same
  Sign/magnitude representation
    Need both addition and subtraction
      Can convert magnitude to 2’s complement to avoid subtraction
    Set sign correctly after compute new mantissa
  Reset to scientific form
Multiplication (Division?)
  Multiply mantissas (keep track of “.”)
  Add exponents
  Set sign correctly
  Reset to scientific form