## Slide 1: Assembly Programming
Abhishek Bhattacharjee
Topics
  Introduction to Assembly Programming
    x86 assembly

## Slide 2: Understanding arith
int arith
(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}
movl 8(%ebp),%eax # eax = x
movl 12(%ebp),%edx # edx = y
leal (%edx,%eax),%ecx # ecx = x+y (t1)
leal (%edx,%edx,2),%edx # edx = 3*y
sall $4,%edx # edx = 48*y (t4)
addl 16(%ebp),%ecx # ecx = z+t1 (t2)
leal 4(%edx,%eax),%eax # eax = 4+t4+x (t5)
imull %ecx,%eax # eax = t5*t2 (rval)
y
x
Rtn adr
Old %ebp
%ebp
0
4
8
12
Offset
Stack
•
•
•
z
16

## Slide 3: Understanding arith
int arith
(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}
# eax = x
movl 8(%ebp),%eax
# edx = y
movl 12(%ebp),%edx
# ecx = x+y (t1)
leal (%edx,%eax),%ecx
# edx = 3*y
leal (%edx,%edx,2),%edx
# edx = 48*y (t4)
sall $4,%edx
# ecx = z+t1 (t2)
addl 16(%ebp),%ecx
# eax = 4+t4+x (t5)
leal 4(%edx,%eax),%eax
# eax = t5*t2 (rval)
imull %ecx,%eax

## Slide 4: Condition Codes
Single Bit Registers
  CF Carry Flag SF Sign Flag
  ZF Zero Flag OF Overflow Flag
Can be set either implicitly or explicitly.
  Implicitly by almost all logic and arithmetic operations
  Explicitly by specific comparison operations
Not Set by leal instruction
  Intended for use in address computation only

## Slide 5: Jumping
jX Instructions
  Jump to different part of code depending on condition codes

## Slide 6: Conditional Branch Example
int max(int x, int y)
{
if (x > y)
return x;
else
return y;
}
_max:
pushl %ebp
movl %esp,%ebp
movl 8(%ebp),%edx
movl 12(%ebp),%eax
cmpl %eax,%edx
jle L9
movl %edx,%eax
L9:
movl %ebp,%esp
popl %ebp
ret
Body
Set
Up
Finish

## Slide 7: “Do-While” Loop Example
C Code
int fact_do
(int x)
{
int result = 1;
do {
result *= x;
x = x-1;
} while (x > 1);
return result;
}
Goto Version
int fact_goto(int x)
{
int result = 1;
loop:
result *= x;
x = x-1;
if (x > 1)
goto loop;
return result;
}
  Use backward branch to continue looping
  Only take branch when “while” condition holds

## Slide 8: “Do-While” Loop Compilation
Goto Version
int fact_goto
(int x)
{
int result = 1;
loop:
result *= x;
x = x-1;
if (x > 1)
goto loop;
return result;
}
Registers
  %edx x
  %eax result
_fact_goto:
pushl %ebp # Setup
movl %esp,%ebp # Setup
movl $1,%eax # eax = 1
movl 8(%ebp),%edx # edx = x
L11:
imull %edx,%eax # result *= x
decl %edx # x--
cmpl $1,%edx # Compare x : 1
jg L11 # if > goto loop
movl %ebp,%esp # Finish
popl %ebp # Finish
ret # Finish
Assembly

## Slide 9: General “Do-While” Translation
C Code
do
Body
while (Test);
Goto Version
loop:
Body
if (Test)
goto loop
  Body can be any C statement
    Typically compound statement:
  Test is expression returning integer
    = 0 interpreted as false 0 interpreted as true
{
Statement1;
Statement2;
…
Statementn;
}

## Slide 10: Actual “While” Loop Translation
C Code
int fact_while(int x)
{
int result = 1;
while (x > 1) {
result *= x;
x = x-1;
};
return result;
}
Second Goto Version
int fact_while_goto2
(int x)
{
int result = 1;
if (!(x > 1))
goto done;
loop:
result *= x;
x = x-1;
if (x > 1)
goto loop;
done:
return result;
}
  Uses same inner loop as do-while version
  Guards loop entry with extra test

## Slide 11: General “While” Translation
C Code
while (Test)
Body
Do-While Version
if (!Test)
goto done;
do
Body
while(Test);
done:
Goto Version
if (!Test)
goto done;
loop:
Body
if (Test)
goto loop;
done:

## Slide 12: Switch Statements
Implementation Options
  Series of conditionals
    Good if few cases
    Slow if many
  Jump Table
    Lookup branch target
    Avoids conditionals
    Possible when cases are small integer constants
  GCC
    Picks one based on case structure
  Bug in example code
    No default given
typedef enum
{ADD, MULT, MINUS, DIV, MOD, BAD}
op_type;
char unparse_symbol(op_type op)
{
switch (op) {
case ADD :
return '+';
case MULT:
return '*';
case MINUS:
return '-';
case DIV:
return '/';
case MOD:
return '%';
case BAD:
return '?';
}
}

## Slide 13: Jump Table Structure
Code Block
0
Targ0:
Code Block
1
Targ1:
Code Block
2
Targ2:
Code Block
n–1
Targn-1:
•
•
•
Targ0
Targ1
Targ2
Targn-1
•
•
•
jtab:
target = JTab[op];
goto *target;
switch(op) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
Approx. Translation
Jump Table
Jump Targets

## Slide 14: Switch Statement Example
Branching Possibilities
Setup:
unparse_symbol:
pushl %ebp # Setup
movl %esp,%ebp # Setup
movl 8(%ebp),%eax # eax = op
cmpl $5,%eax # Compare op : 5
ja .L49 # If > goto done
jmp *.L57(,%eax,4) # goto Table[op]
Enumerated Values
  ADD 0
  MULT 1
  MINUS 2
  DIV 3
  MOD 4
  BAD 5
typedef enum
{ADD, MULT, MINUS, DIV, MOD, BAD}
op_type;
char unparse_symbol(op_type op)
{
switch (op) {
• • •
}
}

## Slide 15: Assembly Setup Explanation
Table Structure
  Each target requires 4 bytes
  Base address at .L57
Jumping
  jmp .L49
    Jump target is denoted by label .L49
  jmp *.L57(,%eax,4)
    Start of jump table denoted by label .L57
    Register %eax holds op
    Must scale by factor of 4 to get offset into table
    Fetch target from effective Address .L57 + op*4

## Slide 16: Jump Table
Enumerated Values
  ADD 0
  MULT 1
  MINUS 2
  DIV 3
  MOD 4
  BAD 5
.section .rodata
.align 4
.L57:
.long .L51 #Op = 0
.long .L52 #Op = 1
.long .L53 #Op = 2
.long .L54 #Op = 3
.long .L55 #Op = 4
.long .L56 #Op = 5
Table Contents
.L51:
movl $43,%eax # ’+’
jmp .L49
.L52:
movl $42,%eax # ’*’
jmp .L49
.L53:
movl $45,%eax # ’-’
jmp .L49
.L54:
movl $47,%eax # ’/’
jmp .L49
.L55:
movl $37,%eax # ’%’
jmp .L49
.L56:
movl $63,%eax # ’?’
# Fall Through to .L49
Targets & Completion

## Slide 17: Switch Statement Completion
Puzzle
  What value returned when op is invalid?
Answer
  Register %eax set to op at beginning of procedure
  This becomes the returned value
Advantage of Jump Table
  Can do k-way branch in O(1) operations
.L49: # Done:
movl %ebp,%esp # Finish
popl %ebp # Finish
ret # Finish

## Slide 18: Stack Operation Examples
%esp
%eax
%edx
%esp
%eax
%edx
%esp
%eax
%edx
0x104
555
0x108
0x108
0x10c
0x110
0x104
555
213
213
123
0x108
0x10c
0x110
555
213
123
0x108
0x104
pushl %eax
0x108
0x10c
0x110
213
123
0x104
213
popl %edx
0x108
213

## Slide 19: Procedure Call Example
%esp
%eip
%esp
%eip
0x804854e
0x108
0x108
0x10c
0x110
0x104
0x804854e
0x8048553
123
0x108
0x10c
0x110
123
0x108
call 8048b90
  804854e: e8 3d 06 00 00 call 8048b90 <main>
  8048553: 50 pushl %eax
0x8048b90
0x104
%eip is program counter

## Slide 20: Procedure Return Example
%esp
%eip
0x104
%esp
%eip
0x8048591
0x8048591
0x104
0x104
0x108
0x10c
0x110
0x8048553
123
0x108
0x10c
0x110
123
ret
  8048591: c3 ret
0x108
%eip is program counter
0x8048553
0x8048553

## Slide 21: Call Chain Example
Code Structure
yoo(…)
{
  •
  •
  who();
  •
  •
}
who(…)
{
  • • •
  amI();
  • • •
  amI();
  • • •
}
amI(…)
{
  •
  •
  amI();
  •
  •
}
yoo
who
amI
amI
amI
Call Chain
  Procedure amI recursive
amI

## Slide 22: Stack Frames
Stack
Pointer
%esp
yoo
who
proc
Frame
Pointer
%ebp
Stack
“Top”
Contents
  Local variables
  Return information
  Temporary space
Management
  Space allocated when enter procedure
    “Set-up” code
  Deallocated when return
    “Finish” code
Pointers
  Stack pointer %esp indicates stack top
  Frame pointer %ebp indicates start of current frame
amI

## Slide 23: Stack Operation
Stack
Pointer
%esp
yoo
•
•
•
Frame
Pointer
%ebp
yoo
Call Chain
yoo(…)
{
  •
  •
  who();
  •
  •
}