## Slide 1: CS 211: Computer Architecture Digital Logic
Abhishek Bhattacharjee
Topics:
  Transistors
  Logic Gates
  Combinational Circuits
  Karnaugh Maps
Reading:
  Chapter 4: Section 4.2

## Slide 2: Transistor: Building Block of Computers
Microprocessors contain millions (billions) of transistors
  Intel Pentium 4 (2000): 48 million
  IBM PowerPC 750FX (2002): 38 million
  IBM/Apple PowerPC G5 (2003): 58 million
Logically, each transistor acts as a switch
Combined to implement logic functions
  AND, OR, NOT
Combined to build higher-level structures
  Adder, multiplexer, decoder, register, …
Combined to build processor
Notes: Intel and Pentium are trademarks of Intel Corporation. IBM and PowerPC are trademarks of International Business Machines Corporation. Apple is a trademark of Apple Computer, Inc.

## Slide 3: Simple Switch Circuit
Switch open:
  No current through circuit
  Light is off
  Vout is +2.9V
Switch closed:
  Current flows
  Light is on
  Vout is 0V
Switch-based circuits can easily represent two states:
on/off, open/closed, voltage/no voltage.

## Slide 4: n-type MOS Transistor
MOS = Metal Oxide Semiconductor
  two types: n-type and p-type
n-type
  when Gate has positive voltage, short circuit between #1 and #2
  when Gate has zero voltage, open circuit between #1 and #2
Gate = 1
Gate = 0

## Slide 5: p-type MOS Transistor
p-type is complementary to n-type
  when Gate has positive voltage, open circuit between #1 and #2
  when Gate has zero voltage, short circuit between #1 and #2
Gate = 1
Gate = 0

## Slide 6: Logic Gates
Use transistors to implement logical functions: AND, OR, NOT
Digital symbols:
  recall that we assign a range of analog voltages to each digital (logic) symbol
  assignment of voltage ranges depends on electrical properties of transistors being used
    typical values for "1": +5V, +3.3V, +2.9V
    from now on we'll use +2.9V

## Slide 7: CMOS Circuit
Complementary MOS
Uses both n-type and p-type MOS transistors
  p-type
    Attached to + voltage
    Pulls output voltage UP when input is zero
  n-type
    Attached to GND
    Pulls output voltage DOWN when input is one
MOS transistors are combined to form Logic Gates
For all inputs, make sure that output is either connected to GND or to +, but not both!

## Slide 8: Inverter (NOT Gate)
In | Out
0 V | 2.9 V
2.9 V | 0 V
In | Out
0 | 1
1 | 0
Truth table

## Slide 9: NOR Gate
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Note: Serial structure on top, parallel on bottom.

## Slide 10: OR Gate
Add inverter to NOR.
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 11: NAND Gate (AND-NOT)
A | B | C
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Note: Parallel structure on top, serial on bottom.

## Slide 12: AND Gate
Add inverter to NAND.
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 13: Basic Logic Gates Symbols

## Slide 14: Logical Completeness
Can implement ANY truth table with AND, OR, NOT.
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
1. AND combinations that yield a "1" in the truth table.
2. OR the results of the AND gates.
Notes: Note the use of the bubbles (NOT) in the input.

## Slide 15: DeMorgan's Law
Converting AND to OR (with some help from NOT)
Consider the following gate:
A | B |  |  |  | 
0 | 0 | 1 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 1
Same as A+B!
To convert AND to OR
(or vice versa),
invert inputs and output.
Generally, DeMorgan’s Laws:
PQ = P + Q
P + Q = P Q
Notes: If there's time, perhaps discuss how all gates can be implemented with NAND (or NOR).
Therefore, you can implement any truth table using only NAND (or NOR) gates.

## Slide 16: NAND and NOR Functional Completeness
Any gate can be implemented using either NOR or NAND gates.
Why is this important?
  When building a chip, easier to build one with all of the same gates.

## Slide 17: More than 2 Inputs?
AND/OR can take any number of inputs.
  AND = 1 if all inputs are 1.
  OR = 1 if any input is 1.
  Similar for NAND/NOR.
Can implement with multiple two-input gates or with single CMOS circuit.
Notes: NAND and NOR are not associative.
Jim Conrad’s example:
NAND(NAND(0,0), 1) = NAND(1, 1) = 0
NAND(0, NAND(0,1)) = NAND(0, 0) = 1

## Slide 18: Decoder
n inputs, 2n outputs
  exactly one output is 1 for each possible input pattern
2-bit
decoder
Notes: Uses of decoder:
convert memory/register address to a control line that selects that location
convert an opcode to one of n control lines

## Slide 19: Multiplexer (MUX)
n-bit selector and 2n inputs, one output
  output equals one of the inputs, depending on selector
4-to-1 MUX
Notes: Another view: decode S, and AND each output with one of the MUX inputs.
Also explain multi-bit inputs.
Uses of multiplexer:
select which input to use for function
select which computed value to pass to next stage (or to place on bus)

## Slide 20: Full Adder
Add two bits and carry-in, produce one-bit sum and carry-out.
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Notes: A half-adder is one that doesn't take a carry-in.
Sum is one when 1 or 3 inputs are one. Carry-out is one when 2 or 3 inputs are one.

## Slide 21: Four-bit Adder
Notes: This is called a "ripple-carry" adder. The sum becomes valid as the carry ripples its way from the low bit to the high bit. How many gate delays until the output is settled?

## Slide 22: Circuit Design
Have a good idea. What kind of circuit might be useful?
Derive a truth table for this circuit
Derive a Boolean expression for the truth table
Build a circuit given the Boolean expression
  Building the circuit involves mapping the Boolean expression to actual gates. This part is easy.
  Deriving the Boolean expression is easy. Deriving a good one is tricky.

## Slide 23: Converting Truth Table to Boolean Expression
Given a circuit, isolate the rows in which the output of the circuit should be true

## Slide 24: Converting Truth Table to Boolean Expression
Given a circuit, isolate that rows in which the output of the circuit should be true
A product term that contains exactly one instance of every variable is called a minterm

## Slide 25: Converting Truth Table to Boolean Expression
Given the expressions for each row, build a larger Boolean expression for the entire table.
  This is a sum-of-products (SOP) form.

## Slide 26: Converting Truth Table to Boolean Expression
Finally build the circuit.
  Problem: SOP forms are often not minimal.
  Solution: Make it minimal. We’ll go over two ways.

## Slide 27: First Approach: Algebraic
Simply use the rules of Boolean logic

## Slide 28: The Result

## Slide 29: Karnaugh Maps or K-Maps
K-maps are a graphical technique to view minterms and how they relate.
The “map” is a diagram made up of squares, with each square representing a single minterm.
Minterms resulting in a “1” are marked as “1”, all others are marked “0”

## Slide 30: 2 Variable K-Map

## Slide 31: 2 Variable K-Map

## Slide 32: 2 Variable K-Map
0
0
1
1

## Slide 33: Finding Commonality

## Slide 34: Finding the “best” solution
Grouping become simplified products.
Both are “correct”. “A+B” is preferred.

## Slide 35: Simplify Example

## Slide 36: Simplify Example

## Slide 37: 3 Variable K-Maps
  Note in higher maps, several variables occupy a given axis
  The sequence of 1s and 0s follow a Gray Code Sequence.
C
B

## Slide 38: 3 Variable K-Maps

## Slide 39: 3 Variable K-Maps
C
B

## Slide 40: 3 Variable K-Maps

## Slide 41: 3 Variable K-Maps

## Slide 42: 3 Variable K-Maps

## Slide 43: Back to our earlier example…..
The K-map and the algebraic produce the same result.

## Slide 44: Up… up… and let’s keep going
B
A
D
C

## Slide 45: Few more examples
B
A
D
C

## Slide 46: Few more examples
B
A
D
C