## Slide 1: CS 211: Computer Architecture Digital Logic: Sequential Circuits and Finite State Machines
Abhishek Bhattacharjee
Reading:
  Uploaded materials on Sakai

## Slide 2: Quick Review

## Slide 3: Bit Storage Summary
We considered increasingly better bit storage until we arrived at the robust D flip-flop bit storage

## Slide 4: Flip-Flop versus Latch

## Slide 5: Master Slave D Flip Flop

## Slide 6: T Flip-Flop
This is a toggle flip-flop – when input T is 1, toggle output Q
Can be realized with a D flip-flop

## Slide 7: JK Flip-Flop
The JK Flip-Flop can also be derived from the basic D Flip-Flop
Its purpose it to combine aspects of the SR Flip-Flop and the T Flip-Flop
  Behaves like an SR flip-flop for all values except J=K=1 (in these cases J = S, and K = R)
  For J = K = 1, it toggles like a T flip flop
  It can be built from a D flip flop

## Slide 8: Flip-Flop Conversion
The purpose is to convert a given type A flip-flop to a desired type B flip-flop using conversion logic
The key is to use excitation tables, which show the necessary triggering signal (S, R, J, K, D, and T) for the desired flip-flop transition

## Slide 9: Excitation Tables
Q(t) | Q(t+1) | S | R | J | K | D | T
0 | 0 | 0 | x | 0 | x | 0 | 0
0 | 1 | 1 | 0 | 1 | x | 1 | 1
1 | 0 | 0 | 1 | x | 1 | 0 | 1
1 | 1 | x | 0 | x | 0 | 1 | 0
This is the combination of input assignments (S, R, J, K, D, and T) required to realize state transitions

## Slide 10: Convert a D-FF to a T-FF
We need to design the circuit to generate the triggering signal D as a function of T and Q  D = f(T, Q)
Consider the excitation tables of T and D
Make a k-map
Q(t)/T | 0 | 1
0 | 0 | 1
1 | 1 | 0
D = T’Q + TQ’ = T xor Q

## Slide 11: Register File
Internal design uses drivers and bus
a
a
d0
d1
d2
d3
e
i0
d0
d1
d2
d3
W_en
W_addr
W_data
i1
2x4
32
32
32
32
32
32
i1
i0
e
2x4
load
load
load
load
reg0
reg1
reg2
reg3
R_en
R_addr
R_data
driver
bus
write
decoder
read
decoder
4x32 register file
Internal design of 4x32 RF; 16x32 RF follows similarly
q
c=1: q=d
c
c=0: q= Z
¢
d
¢
d
q
d
q
like no connection
three-state driver
q
q=d
d
driver
Boosts signal
Note: Each driver in figure actually represents 32 1-bit drivers

## Slide 12: Finite State Machines
FSM = State register + combinational logic
Stores the next state and
loads the next state at
clock edge
Computes the next state
and computes the outputs

## Slide 13: Traffic Light Controller Example

## Slide 14: FSM State Transition Diagram

## Slide 15: FSM State Transition Table
State transitions from diagram can be rewritten in a state transition table

## Slide 16: Encoded State Transition Table
After selecting a state encoding, the symbolic states in the transition table can be realized with current state/next state bits

## Slide 17: Computing Next State Logic
From K-maps, figure out expressions for the next state:
S1(t+1) = S1(t) xor S0(t)
S0(t+1) = S1’(t) S0’(t) TA + S1’(t) S0’(t) TB
Another way of writing the same thing (just a change of notation):

## Slide 18: FSM Output Table
FSM output logic is computed in similar manner as next state logic
In this system, output is a function of current state (Moore machine)
Alternative – Mealy machine (output function of both current state and inputs, though we won’t cover this in class)

## Slide 19: State Register: Assume D-FF

## Slide 20: FSM: Figure out Next State Logic

## Slide 21: FSM: Figure out Output Logic

## Slide 22: FSM Example 2
Design an FSM that detects a stream of three or more consecutive 1s on an input stream
Input: 0 1 1 1 0 1 0 1 1 0 1 1 1 0 1 …
Output: 0 0 0 1 0 0 0 0 0 0 0 0 1 0 0 …

## Slide 23: FSM: State Diagram
State
Diagram

## Slide 24: FSM Design: Truth Tables
QA
QB
QA+
QB+
State Table

## Slide 25: FSM: Assuming D-Flip Flops for State

## Slide 26: FSM Design: Example (Moore)
QA
QB
Q'B

## Slide 27: FSM Design: What if we have JK Flip Flops, not D Flip Flops
+
Excitation Table

## Slide 28: Assume we have the following NEW State Table: With JK Flip Flops

## Slide 29: FSM Design: JK Flip Flops

## Slide 30: FSM Design: JK Flip Flops
QA
QB
Q'B
Q'A