## Slide 1: CS 211: Computer Architecture Memory Hierarchy & Caching
Abhishek Bhattacharjee
Topics
  Storage technologies and trends
  Locality of reference
  Caching in the memory hierarchy
Reading:
  Chapter 6: Introduction, 6.1.1, 6.2-6.4

## Slide 2: Memory
Thus far, we have used a very simple model of memory
  Main Memory is a linear array of bytes that can be accessed given a memory address
  Also used registers to store values
Reality is more complex. There is an entire memory system.
  Different memories exist at different levels of the computer
  Each vary in their speed, size, and cost

## Slide 3: Random-Access Memory (RAM)
Key features
  RAM is packaged as a chip.
  Basic storage unit is a cell (one bit per cell).
  Multiple RAM chips form a memory.
Static RAM (SRAM)
  Each cell stores bit with a six-transistor circuit.
  Retains value indefinitely, as long as it is kept powered.
  Relatively insensitive to disturbances such as electrical noise.
  Faster and more expensive than DRAM.
Dynamic RAM (DRAM)
  Each cell stores bit with a capacitor and transistor.
  Value must be refreshed every 10-100 ms.
  Sensitive to disturbances.
  Slower and cheaper than SRAM.

## Slide 4: Memory speeds
Processor Speeds : 1 GHz processor speed is 1 nsec cycle time.
Memory Speeds (50 nsec)
DIMM Module Clock Speed[MHz] Bus Speed[ MHz] Transfer Rate [MB/s]
PC1600 DDR200 100 200 1,600
PC2100 DDR266 133 266 2,133
PC2400 DDR300 150 300 2,400
Access Speed gap
  Instructions that store or load from memory

## Slide 5: Conventional DRAM Organization
d x w DRAM:
  dw total bits organized as d supercells of size w bits
cols
rows
0
1
2
3
0
1
2
3
internal row buffer
16 x 8 DRAM chip
addr
data
supercell
(2,1)
4 bits
/
8 bits
/
memory
controller
(to CPU)

## Slide 6: Reading DRAM Supercell (2,1)
Step 1(a): Row access strobe (RAS) selects row 2
Step 1(b): Row 2 copied from DRAM array to row buffer
cols
rows
RAS = 2
0
1
2
3
0
1
2
internal row buffer
16 x 8 DRAM chip
3
addr
data
2
/
8
/
memory
controller

## Slide 7: Reading DRAM Supercell (2,1)
Step 2(a): Column access strobe (CAS) selects column 1
Step 2(b): Supercell (2,1) copied from buffer to data lines, and eventually back to the CPU
cols
rows
0
1
2
3
0
1
2
3
internal row buffer
16 x 8 DRAM chip
CAS = 1
addr
data
2
/
8
/
memory
controller
supercell
(2,1)
supercell
(2,1)
To CPU

## Slide 8: Memory Modules
We’ve been discussing single DRAM Chips
Several DRAM chips are bundled into Memory Modules
  SIMMS - Single Inline Memory Module
  DIMMS - Dual Inline Memory Module
Source for Pictures: http://en.kioskea.net/contents/pc/ram.php3

## Slide 9: Machine Architecture
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus
Expansion slots for
other devices such
as network adapters
PC
Input
Output

## Slide 10: System/Memory Bus
A bus is a collection of parallel wires that carry address, data, and control signals
Buses are typically shared by multiple devices
Information passed through transactions
main
memory
I/O
bridge
bus interface
ALU
register file
CPU chip
system bus
memory bus

## Slide 11: Memory Read Transaction (1)
CPU places address A on the memory bus.
ALU
register file
bus interface
A
0
A
x
main memory
I/O bridge
%eax
Load operation: movl A, %eax

## Slide 12: Memory Read Transaction (2)
Main memory reads A from the memory bus, retreives word x, and places it on the bus.
ALU
register file
bus interface
x
0
A
x
main memory
%eax
I/O bridge
Load operation: movl A, %eax

## Slide 13: Memory Read Transaction (3)
CPU read word x from the bus and copies it into register %eax.
x
ALU
register file
bus interface
x
main memory
0
A
%eax
I/O bridge
Load operation: movl A, %eax

## Slide 14: Memory Write Transaction (1)
CPU places address A on bus. Main memory reads it and waits for the corresponding data word to arrive.
y
ALU
register file
bus interface
A
main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 15: Memory Write Transaction (2)
CPU places data word y on the bus.
y
ALU
register file
bus interface
y
main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 16: Memory Write Transaction (3)
Main memory read data word y from the bus and stores it at address A.
y
ALU
register file
bus interface
y
main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 17: Memory Hierarchy (Review)
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
remote secondary storage
(distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers.
Main memory holds disk
blocks retrieved from local
disks.
off-chip L2
cache (SRAM)
L1 cache holds cache lines retrieved from the L2 cache memory.
CPU registers hold words retrieved from L1 cache.
L2 cache holds cache lines retrieved from main memory.
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices

## Slide 18: Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware
  Hold frequently accessed blocks of main memory
CPU looks first for data in L1, then in L2, then in main memory
main
memory
I/O
bridge
bus interface
L2 cache
ALU
register file
CPU chip
cache bus
system bus
memory bus
L1
cache

## Slide 19: Locality
Memory references are bunched together
  A small portion of address space is accessed at any given time
Cache this portion of the address space in faster memories
Processor

## Slide 20: Types of Locality
Temporal locality
  Recently accessed locations will likely be accessed again in near future
Spatial locality
  Will likely access locations close to ones recently accessed in near future
X
X
X
t

## Slide 21: Sources of Locality
Temporal locality
  Code within a loop
  Same instructions fetched repeatedly
Spatial locality
  Data arrays
  Local variables in stack
  Data allocated in chunks (contiguous bytes)

## Slide 22: Why Is Locality Good?
Address the gap between CPU speed and RAM speed
Spatial and temporal locality implies a portion of overall address space can fit in high speed memory
CPU can access instructions and data from this high speed memory
Small high speed memory can make computer faster and cheaper
This is caching

## Slide 23: Caching in a Memory Hierarchy
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Larger, slower, cheaper storage
device at level k+1 is partitioned
into blocks.
Data is copied between
levels in block-sized transfer units
8
9
14
3
Smaller, faster, more expensive
device at level k caches a
subset of the blocks from level k+1
Level k:
Level k+1:
4
4
4
10
10
10

## Slide 24: General Caching Concepts
Request
14
Request
12
Program needs object d, which is stored in some block b.
Cache hit
  Program finds b in the cache at level k. E.g., block 14.
Cache miss
  b is not at level k, so level k cache must fetch it from level k+1. E.g., block 12.
  If level k cache is full, then some current block must be replaced (evicted). Which one is the “victim”?
    Placement policy: where can the new block go? E.g., b mod 4
    Replacement policy: which block should be evicted? E.g., LRU
9
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Level
k:
Level
k+1:
14
14
12
14
4*
4*
12
12
0
1
2
3
Request
12
4*
4*
12

## Slide 25: Cache Miss
Cold (compulsary) miss
  Cold miss occurs when a memory location is accessed for the 1st time
Conflict miss
  Most caches limit blocks at level k+1 to a small subset of the block positions at level k.
    E.g., Block i at level k+1 must be placed in block (i mod 4) at level k+1
  Conflict misses occur when the level k cache is large enough, but multiple data items all map to the same level k block.
    E.g., Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time
Capacity miss
  Occurs when the set of active data blocks (working set) is larger than the cache

## Slide 26
local secondary storage
(local disks)
L4:
registers
L0:
on-chip L1
cache (SRAM)
L1:
off-chip L2
cache (SRAM)
L2:
main memory
(DRAM)
L3:
Remember:
  Each level is a cache for previous
  Each level stores different sizes of information
Request for A
A
B
C

## Slide 27: L1 Cache
a b c d
block 10
p q r s
block 21
...
...
w x y z
block 30
...
The big slow main memory
has room for many 4-word
blocks.
The small fast L1 cache has room
for two 4-word blocks.
The tiny, very fast CPU register file
has room for four 4-byte words.
The transfer unit between
the cache and main
memory is a 4-word block
(16 bytes).
The transfer unit between
the CPU register file and
the cache is a 4-byte block.
line 0
line 1

## Slide 28: Cache Content
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
You are essentially allowing a smaller region of memory to hold data from a larger region. Not a 1-1 mapping.
What kind of information do we need to keep:
  The actual data
  Where the data actually comes from
  If data is even considered valid

## Slide 29: Cache Mapping
Multiple locations in memory map to same location in cache
In addition to content, cache must keep which entry it is actually caching
Memory
Cache

## Slide 30: Finding data in cache
Part of memory address applied to cache
Remaining is stored as tag in cache
If tag matches, hit, use data
No match, miss, fetch data from memory
address
tag

## Slide 31: General Org of a Cache Memory
• • •
B–1
1
0
• • •
B–1
1
0
valid
valid
tag
tag
set 0:
B = 2b bytes
per cache block
E lines
per set
S = 2s sets
t tag bits
per line
1 valid bit
per line
Cache size: C = B x E x S data bytes
• • •
• • •
B–1
1
0
• • •
B–1
1
0
valid
valid
tag
tag
set 1:
• • •
• • •
B–1
1
0
• • •
B–1
1
0
valid
valid
tag
tag
set S-1:
• • •
• • •
Cache is an array
of sets.
Each set contains
one or more lines.
Each line holds a
block of data.

## Slide 32: Addressing Caches
t bits
s bits
b bits
0
m-1
<tag>
<set index>
<block offset>
Address A:
• • •
B–1
1
0
• • •
B–1
1
0
v
v
tag
tag
set 0:
• • •
• • •
B–1
1
0
• • •
B–1
1
0
v
v
tag
tag
set 1:
• • •
• • •
B–1
1
0
• • •
B–1
1
0
v
v
tag
tag
set S-1:
• • •
• • •
The word at address A is in the cache if
the tag bits in one of the <valid> lines in
set <set index> match <tag>.
The word contents begin at offset
<block offset> bytes from the beginning
of the block.

## Slide 33: Direct-Mapped Cache
Simplest kind of cache
Characterized by exactly one line per set.
valid
valid
valid
tag
tag
tag
• • •
set 0:
set 1:
set S-1:
E=1 lines per set
cache block
cache block
cache block

## Slide 34: Accessing Direct-Mapped Caches
Set selection
  Use the set index bits to determine the set of interest.
valid
valid
valid
tag
tag
tag
• • •
set 0:
set 1:
set S-1:
t bits
s bits
0 0 0 0 1
b bits
tag
set index
block offset
selected set
cache block
cache block
cache block

## Slide 35: Accessing Direct-Mapped Caches
Line matching and word selection
  Line matching: Find a valid line in the selected set with a matching tag
  Word selection: Then extract the word
1
t bits
s bits
100
i
0110
b bits
tag
set index
block offset
selected set (i):
(3) If (1) and (2), then
cache hit,
and block offset
selects
starting byte.
=1?
(1) The valid bit must be set
= ?
(2) The tag bits in the cache
line must match the
tag bits in the address
0110
w3
w0
w1
w2
3
0
1
2
7
4
5
6

## Slide 36: Why Use Middle Bits as Index?
High-Order Bit Indexing
  Adjacent memory lines would map to same cache entry
  Poor use of spatial locality
Middle-Order Bit Indexing
  Consecutive memory lines map to different cache lines
  Can hold C-byte region of address space in cache at one time
4-line Cache
High-Order
Bit Indexing
Middle-Order
Bit Indexing
00
01
10
11
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111

## Slide 37: Direct-Mapped Cache Simulation
M=16 bit addresses, B=2 bytes/block,
S=4 sets, E=1 entry/set
Address trace (reads):
0 [00002], 1 [00012], 13 [11012], 8 [10002], 0 [00002]
x
t=1
s=2
b=1
xx
x
1
0
m[1] m[0]
v
tag
data
0 [00002] (miss)
(1)
1
0
m[1] m[0]
v
tag
data
1
1
m[13] m[12]
13 [11012] (miss)
(3)
1
1
m[9] m[8]
v
tag
data
8 [10002] (miss)
(4)
1
0
m[1] m[0]
v
tag
data
1
1
m[13] m[12]
0 [00002] (miss)
(5)
0
M[0-1]
1
1
M[12-13]
1
1
M[8-9]
1
1
M[12-13]
1
0
M[0-1]
1
1
M[12-13]
1
0
M[0-1]
1