## Slide 1: CS 211: Computer Architecture Memory Hierarchy & Caching
Abhishek Bhattacharjee
Topics
  Storage technologies and trends
  Locality of reference
  Caching in the memory hierarchy
Reading:
  Chapter 6: Introduction, 6.1.1, 6.2-6.4

## Slide 2
local secondary storage
(local disks)
L4:
registers
L0:
on-chip L1
cache (SRAM)
L1:
off-chip L2
cache (SRAM)
L2:
main memory
(DRAM)
L3:
Remember:
  Each level is a cache for previous
  Each level stores different sizes of information
Request for A
A
B
C

## Slide 3: L1 Cache
a b c d
block 10
p q r s
block 21
...
...
w x y z
block 30
...
The big slow main memory
has room for many 4-word
blocks.
The small fast L1 cache has room
for two 4-word blocks.
The tiny, very fast CPU register file
has room for four 4-byte words.
The transfer unit between
the cache and main
memory is a 4-word block
(16 bytes).
The transfer unit between
the CPU register file and
the cache is a 4-byte block.
line 0
line 1

## Slide 4: Cache Content
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
You are essentially allowing a smaller region of memory to hold data from a larger region. Not a 1-1 mapping.
What kind of information do we need to keep:
  The actual data
  Where the data actually comes from
  If data is even considered valid

## Slide 5: Cache Mapping
Multiple locations in memory map to same location in cache
In addition to content, cache must keep which entry it is actually caching
Memory
Cache

## Slide 6: Finding data in cache
Part of memory address applied to cache
Remaining is stored as tag in cache
If tag matches, hit, use data
No match, miss, fetch data from memory
address
tag

## Slide 7: General Org of a Cache Memory
• • •
B–1
1
0
• • •
B–1
1
0
valid
valid
tag
tag
set 0:
B = 2b bytes
per cache block
E lines
per set
S = 2s sets
t tag bits
per line
1 valid bit
per line
Cache size: C = B x E x S data bytes
• • •
• • •
B–1
1
0
• • •
B–1
1
0
valid
valid
tag
tag
set 1:
• • •
• • •
B–1
1
0
• • •
B–1
1
0
valid
valid
tag
tag
set S-1:
• • •
• • •
Cache is an array
of sets.
Each set contains
one or more lines.
Each line holds a
block of data.

## Slide 8: Addressing Caches
t bits
s bits
b bits
0
m-1
<tag>
<set index>
<block offset>
Address A:
• • •
B–1
1
0
• • •
B–1
1
0
v
v
tag
tag
set 0:
• • •
• • •
B–1
1
0
• • •
B–1
1
0
v
v
tag
tag
set 1:
• • •
• • •
B–1
1
0
• • •
B–1
1
0
v
v
tag
tag
set S-1:
• • •
• • •
The word at address A is in the cache if
the tag bits in one of the <valid> lines in
set <set index> match <tag>.
The word contents begin at offset
<block offset> bytes from the beginning
of the block.

## Slide 9: Direct-Mapped Cache
Simplest kind of cache
Characterized by exactly one line per set.
valid
valid
valid
tag
tag
tag
• • •
set 0:
set 1:
set S-1:
E=1 lines per set
cache block
cache block
cache block

## Slide 10: Accessing Direct-Mapped Caches
Set selection
  Use the set index bits to determine the set of interest.
valid
valid
valid
tag
tag
tag
• • •
set 0:
set 1:
set S-1:
t bits
s bits
0 0 0 0 1
b bits
tag
set index
block offset
selected set
cache block
cache block
cache block

## Slide 11: Accessing Direct-Mapped Caches
Line matching and word selection
  Line matching: Find a valid line in the selected set with a matching tag
  Word selection: Then extract the word
1
t bits
s bits
100
i
0110
b bits
tag
set index
block offset
selected set (i):
(3) If (1) and (2), then
cache hit,
and block offset
selects
starting byte.
=1?
(1) The valid bit must be set
= ?
(2) The tag bits in the cache
line must match the
tag bits in the address
0110
w3
w0
w1
w2
3
0
1
2
7
4
5
6

## Slide 12: Why Use Middle Bits as Index?
High-Order Bit Indexing
  Adjacent memory lines would map to same cache entry
  Poor use of spatial locality
Middle-Order Bit Indexing
  Consecutive memory lines map to different cache lines
  Can hold C-byte region of address space in cache at one time
4-line Cache
High-Order
Bit Indexing
Middle-Order
Bit Indexing
00
01
10
11
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111

## Slide 13: Direct-Mapped Cache Simulation
M=16 bit addresses, B=2 bytes/block,
S=4 sets, E=1 entry/set
Address trace (reads):
0 [00002], 1 [00012], 13 [11012], 8 [10002], 0 [00002]
x
t=1
s=2
b=1
xx
x
1
0
m[1] m[0]
v
tag
data
0 [00002] (miss)
(1)
1
0
m[1] m[0]
v
tag
data
1
1
m[13] m[12]
13 [11012] (miss)
(3)
1
1
m[9] m[8]
v
tag
data
8 [10002] (miss)
(4)
1
0
m[1] m[0]
v
tag
data
1
1
m[13] m[12]
0 [00002] (miss)
(5)
0
M[0-1]
1
1
M[12-13]
1
1
M[8-9]
1
1
M[12-13]
1
0
M[0-1]
1
1
M[12-13]
1
0
M[0-1]
1

## Slide 14: Set Associative Caches
Characterized by more than one line per set
valid
tag
set 0:
E=2 lines per set
set 1:
set S-1:
• • •
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block

## Slide 15: Accessing Set Associative Caches
Set selection
  identical to direct-mapped cache
valid
valid
tag
tag
set 0:
valid
valid
tag
tag
set 1:
valid
valid
tag
tag
set S-1:
• • •
t bits
s bits
0 0 0 0 1
0
m-1
b bits
tag
set index
block offset
Selected set
cache block
cache block
cache block
cache block
cache block
cache block

## Slide 16: Accessing Set Associative Caches
Line matching and word selection
  must compare the tag in each valid line in the selected set.
1
0110
w3
w0
w1
w2
1
1001
t bits
s bits
100
i
0110
0
m-1
b bits
tag
set index
block offset
selected set (i):
=1?
(1) The valid bit must be set.
= ?
(2) The tag bits in one
of the cache lines must
match the tag bits in
the address
(3) If (1) and (2), then
cache hit, and
block offset selects
starting byte.
3
0
1
2
7
4
5
6

## Slide 17: Accessing Set Associative Caches
Line matching and word selection
  must compare the tag in each valid line in the selected set.
1
0110
w3
w0
w1
w2
1
1001
t bits
s bits
100
i
0110
0
m-1
b bits
tag
set index
block offset
selected set (i):
=1?
(1) The valid bit must be set.
= ?
(2) The tag bits in one
of the cache lines must
match the tag bits in
the address
(3) If (1) and (2), then
cache hit, and
block offset selects
starting byte.
3
0
1
2
7
4
5
6
Why all of this extra work? Any other issues?

## Slide 18: Replacement
What if has a cache miss but all entries in the set are valid?
Direct-mapped cache: no decision
  Discard current content and bring needed content in
Set Associate cache: which line to evict?
  Need a replacement algorithm
If we knew the future, can you think of an optimal replacement algorithm?
Since we are oracles, we need to approximate
  FIFO: First-In-First-Out
  LRU: Least Recently Used
  Random: Select victim from set randomly

## Slide 19: Replacement
How would you implement FIFO replacement in software?
How would you implement LRU replacement in software?
How would you implement these algorithms in hardware?

## Slide 20: Fully Associative Caches
Set selection is trivial
Accessing a line is the same as a set associative cache
valid
valid
tag
tag
set 0:
valid
valid
tag
tag
valid
valid
tag
tag
• • •
cache block
cache block
cache block
cache block
cache block
cache block

## Slide 21: Example: Direct mapped cache
32 bit address, 64KB cache, 32 byte block
How many sets, how many bits for the tag, how many bits for the offset?
valid
valid
valid
tag
tag
tag
• • •
set 0:
set 1:
cache block
cache block
cache block
set n-1:

## Slide 22: Example: 2-way associative cache
32 bit address, 64KB cache, 32 byte block
How many sets (lines), how many bits for the tag, how many bits for the offset?
valid
tag
set 0:
E=2 lines per set
set 1:
set S-1:
• • •
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block

## Slide 23: Example: 2-way associative cache
32 bit address, 32KB cache, 16 byte block
How many sets, how many bits for the tag, how many bits for the offset?
valid
tag
set 0:
E=2 lines per set
set 1:
set S-1:
• • •
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block

## Slide 24: Writes and Cache
Reading information from a cache is straight forward
What about writing?
  What if you’re writing data that is already cached (write-hit)?
  What if the data is not in the cache (write-miss)?
Dealing with a write-hit
  Write-through - immediately write data back to memory
  Write-back - defer the write to memory for as long as possible
Dealing with a write-miss
  write-allocate - load the block into memory and update
  no-write-allocate - writes directly to memory
Write-through caches are typically no-write-allocate
Write-back caches are typically write-allocate

## Slide 25: Write-Back Caches
What happens if we need to evict a block that has been written into?
Need to write cached copy to lower-level
  Hence the name write-back
How do we know whether a block has been written to?
  Add a bit – called the dirty bit
  Set dirty bit when writing to a block
  When evicting a block, need to write to lower-level if dirty bit is set

## Slide 26: Multi-Level Caches
Options: separate data and instruction caches, or a unified cache
Memory
L1
d-cache
Regs
Unified
L2
Cache
Processor
L1
i-cache
disk

## Slide 27: Intel Pentium Cache Hierarchy
Processor Chip
L1 Data
1 cycle latency
16 KB
4-way assoc
Write-through
32B lines
L1 Instruction
16 KB, 4-way
32B lines
Regs.
L2 Unified
128KB--2 MB
4-way assoc
Write-back
Write allocate
32B lines
Main
Memory
Up to 4GB

## Slide 28: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses/references)
  Typical numbers:
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor (includes time to determine whether the line is in the cache)
  Typical numbers:
    1 clock cycle for L1
    3-8 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    Typically 25-100 cycles for main memory

## Slide 29: Miss Types
Cold misses
  When a location is accessed for the 1st time
  Can reduce by increasing block size (leveraging spatial locality)
Conflict misses
  More blocks that map into a single set is concurrently active than can be stored in the set
  Can reduce by increase associativity
Capacity misses
  More blocks are active than can fit into the cache
  Working set
Pre-fetching is a technique that could be used to alleviate all three types of misses
  Predict what will be used next and pre-fetch before actually have a miss
    Large block sizes is a form of prefetching
  If wrong, can worsen performance of cache

## Slide 30: Writing Cache Friendly Code
Repeated references to variables are good (temporal locality)
Stride-1 reference patterns are good (spatial locality)
Examples:
  cold cache, 4-byte words, 4-word cache blocks
int sumarrayrows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
int sumarraycols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
Miss rate =
Miss rate =
1/4 = 25%
100%

## Slide 31: Matrix Multiplication Example
Major Cache Effects to Consider
  Total cache size
    Exploit temporal locality and keep the working set small (e.g., by using blocking)
  Block size
    Exploit spatial locality
Description:
  Multiply N x N matrices
  O(N3) total operations
  Accesses
    N reads per source element
    N values summed per destination
      but may be able to hold in register
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register

## Slide 32: Miss Rate Analysis for Matrix Multiply
Assume:
  Line size = 32B (big enough for 4 64-bit words)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
C
A
k
i
B
k
j
i
j

## Slide 33: Layout of C Arrays in Memory (review)
C arrays allocated in row-major order
  each row in contiguous memory locations
Stepping through columns in one row:
  for (i = 0; i < N; i++)
    sum += a[0][i];
  accesses successive elements
  if block size (B) > 4 bytes, exploit spatial locality
    compulsory miss rate = 4 bytes / B
Stepping through rows in one column:
  for (i = 0; i < n; i++)
    sum += a[i][0];
  accesses distant elements
  no spatial locality!
    compulsory miss rate = 1 (i.e. 100%)

## Slide 34: Matrix Multiplication (ijk)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Misses per Inner Loop Iteration:
  A B C
  0.25 1.0 0.0

## Slide 35: Matrix Multiplication (jik)
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per Inner Loop Iteration:
  A B C
  0.25 1.0 0.0

## Slide 36: Matrix Multiplication (kij)
/* kij */
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per Inner Loop Iteration:
  A B C
  0.0 0.25 0.25

## Slide 37: Matrix Multiplication (ikj)
/* ikj */
for (i=0; i<n; i++) {
for (k=0; k<n; k++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per Inner Loop Iteration:
  A B C
  0.0 0.25 0.25

## Slide 38: Matrix Multiplication (jki)
/* jki */
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Column -
wise
Column-
wise
Fixed
Misses per Inner Loop Iteration:
  A B C
  1.0 0.0 1.0

## Slide 39: Matrix Multiplication (kji)
/* kji */
for (k=0; k<n; k++) {
for (j=0; j<n; j++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Fixed
Column-
wise
Column-
wise
Misses per Inner Loop Iteration:
  A B C
  1.0 0.0 1.0

## Slide 40: Summary of Matrix Multiplication
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
ijk (& jik):
  2 loads, 0 stores
  misses/iter = 1.25
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
kij (& ikj):
  2 loads, 1 store
  misses/iter = 0.5
jki (& kji):
  2 loads, 1 store
  misses/iter = 2.0

## Slide 41: Pentium Matrix Multiply Performance
Miss rates are helpful but not perfect predictors.
    Code scheduling matters, too.

## Slide 42: Improving Temporal Locality by Blocking
Example: Blocked matrix multiplication
  “block” (in this context) does not mean “cache block”.
  Instead, it mean a sub-block within the matrix.
  Example: N = 8; sub-block size = 4
C11 = A11B11 + A12B21 C12 = A11B12 + A12B22
C21 = A21B11 + A22B21 C22 = A21B12 + A22B22
A11 A12
A21 A22
B11 B12
B21 B22
X
=
C11 C12
C21 C22
Key idea: Sub-blocks (i.e., Axy) can be treated just like scalars.

## Slide 43: Pentium Blocked Matrix Multiply Performance
Blocking (bijk and bikj) improves performance by a factor of two over unblocked versions (ijk and jik)
  relatively insensitive to array size.

## Slide 44: Concluding Observations
Programmer can optimize for cache performance
  How data structures are organized
  How data are accessed
    Nested loop structure
    Blocking is a general technique
All systems favor “cache friendly code”
  Getting absolute optimum performance is very platform specific
    Cache sizes, line sizes, associativities, etc.
  Can get most of the advantage with generic code
    Keep working set reasonably small (temporal locality)
    Use small strides (spatial locality)