## Slide 1: Assembly Programming
Abhishek Bhattacharjee
Topics
  Introduction to Assembly Programming
    x86 assembly

## Slide 2: Review

## Slide 3: Decimal to IEEE Floating Point
5.625
In binary
101.101  1.01101 x 22
Exponent field has value 2
  add 127 to get 129
Exponent is 10000001
Mantissa is 01101
Sign bit is 0
0 10000001 0110100000000000000000

## Slide 4: 2’s Complement Addition & Subtraction
Addition = binary addition, ignore carry out
Subtraction = invert subtrahend and add
4 – 2 = 4 + -2
-7 1001
+ 5 0101
----------
-2 1110
-5 1011
+ -2 1110
------------
-7 11001
4 0100
+ -2 1110
------------
2 0010

## Slide 5: 2’s Complement Overflow
What happens when overflow occurs with 2’s complement?
  Need one extra bit so sign bit will be wrong
  How to detect?
    Adding 2 positive numbers  negative result
    Adding 2 negative numbers  positive result
6 0110
+ 5 0101
-----------
-5 1011
-6 1010
+ -6 1010
------------
4 0100

## Slide 6: Multiplication Algorithm
1011
x 101
------
1011
0000
1011
------
110111
(multiplicand x 1) shift left 0
(multiplicand x 0) shift left 1
(multiplicand x 1) shift left 2

## Slide 7: Algorithm
result = 0
If LSB of multiplier = 1, add multiplicand to result else, add 0 to result
Shift multiplicand left by 1 bit (fill LSB with 0)
Shift multiplier right by 1 bit (fill MSB with 0)
If multiplier > 0, go to 1
Stop
We only need to know how to add and shift in order to multiply

## Slide 8: Sign extension
Signed integer | 4-bit representation | 8-bit representation | 16-bit representation
+1 | 0001 | 00000001 | 0000000000000001
-1 | 1111 | 11111111 | 1111111111111111

## Slide 9: Assembly Programming
Brief tour through assembly language programming
Why?
  Machine interface: where software meets hardware
  To understand how the hardware works, we have to understand the interface that it exports
Why not binary language?
  Much easier for humans to read and reason about
  Major differences:
    Human readable language instead of binary sequences
    Relative instead of absolute addresses

## Slide 10: Programming Meets Hardware
High-Level Language Program
Assembly Language Program
Machine Language Program
movl $1, -8(%ebp)
movl $2, -12(%ebp)
movl -8(%ebp), %eax
movl %eax, -16(%ebp)
movl -12(%ebp), %eax
movl %eax, -8(%ebp)
movl -16(%ebp), %eax
movl %eax, -12(%ebp)
movl -16(%ebp), %eax
movl %eax, 12(%esp)
movl -12(%ebp), %eax
movl %eax, 8(%esp)
movl -8(%ebp), %eax
movl %eax, 4(%esp)
7f 45 4c 46 01 01 01
00 00 00 00 00 00 00
00 00 02 00 03 00 01
00 00 00 f0 82 04 08
34 00 00 00 c4 0c 00
00 00 00 00 00 34 00
#include <stdio.h>
int main() {
int x, y, temp;
x=1; y=2;
temp =x; x=y; y=temp;
printf("%d %d %d\n",x,y,temp);
}
ISA
Compiler
Assembler

## Slide 11: IA32
There are many different assembly languages because they are processor-specific
  IA32 (x86)
    x86-64 for new 64-bit processors
    IA-64 radically different for Itanium processors
  PowerPC
  MIPS
We will focus on IA32 because you can generate and run on iLab machines (as well as your own PC/laptop)
  IA32 is also dominant in the market although smart phone, eBook readers, etc. are changing this

## Slide 12: Aside About Implementation of x86
About 30 years ago, the instruction set actually reflected the processor hardware
  E.g., the set of registers in the instruction set is actually what was present in the processor
As hardware advanced, industry faced with choice
  Change the instruction set: bad for backward compatibility
  Keep the instruction set: harder to exploit hardware advances
    Example: many more registers but only small set introduced circa 1980
Starting with the P6 (PentiumPro), IA32 actually got implemented by Intel using an “interpreter” that translates IA32 instructions into a simpler “micro” instruction set

## Slide 13: P6 Decoder/Interpreter

## Slide 14: Assembly Programmer’s View
Control
Logic
(OS code & data)
Object Code
Program Data
Addresses
Data
Instructions
Registers
ALU
CPU
Memory
Condition
Codes
PC

## Slide 15: Memory
00101100
10001000
11111111
01010101
00000000
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
Address
Command: R/W
Data
CPU

## Slide 16: Memory Access: Read
00101100
10001000
11111111
01010101
00000000
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
03
R
CPU
01010101

## Slide 17: Memory Access: Write
00101100
10001000
11111111
01010101
00000000
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
04
W
CPU
01010101

## Slide 18: Memory Access: Write
00101100
10001000
11111111
01010101
01010101
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
04
W
CPU
01010101

## Slide 19: Processor: ALU & Registers
ALU
B
C
A
S
C = FS(A, B)
F includes
Arithmetic: +, -, *, /, ~, etc.
Logical: <, >, =, etc.
00101100
10001000
11111111
01010101
R0
R1
R2
R3
Name
Storage
Registers
Name
Command: R/W
Data
Multiple Ports

## Slide 20: Putting It All Together
ALU
Control
Logic
Registers
Program Counter (PC)
00101100
10001000
11111111
01010101
01010101
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
CPU
Condition Codes

## Slide 21: Putting It All Together
ALU
Control
Logic
Registers
Program Counter (PC)
00101100
10001000
11111111
01010101
01010101
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
CPU
Condition Codes
1

## Slide 22: Putting It All Together
ALU
Control
Logic
Registers
Program Counter (PC)
00101100
10001000
11111111
01010101
01010101
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
CPU
Condition Codes
1
1
10001000

## Slide 23: Putting It All Together
ALU
Control
Logic
Registers
Program Counter (PC)
00101100
10001000
11111111
01010101
01010101
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
CPU
Condition Codes
1
1
10001000
+
R0
R1
R0: x
R1: y

## Slide 24: Putting It All Together
ALU
Control
Logic
Registers
Program Counter (PC)
00101100
10001000
11111111
01010101
01010101
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
CPU
Condition Codes
1
1
10001000
+
R0
R1
x
y
R0: x
R1: y

## Slide 25: Putting It All Together
ALU
Control
Logic
Registers
Program Counter (PC)
00101100
10001000
11111111
01010101
01010101
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
CPU
Condition Codes
2
1
10001000
+
R0
R1
x
y
z
R2: z
R0: x
R1: y
R2

## Slide 26: Basic CPU Function
FETCH[PC++]
DECODE
EXECUTE
Arithmetic: +, -, *, /
Logic: bre, jmp

## Slide 27: Assembly Characteristics
Sequence of simple instructions
Minimal Data Types
  “Integer” data of 1, 2, or 4 bytes
    Data values
    Addresses (untyped pointers)
  Floating point data of 4, 8, or 10 bytes
  No aggregate types such as arrays or structures
    Just contiguously allocated bytes in memory
No type checking
  Interpretation of data format depends on instruction
  No protection against misinterpretation of data

## Slide 28: Assembly Characteristics
Primitive Operations
  Perform arithmetic function on register or memory data
  Transfer data between memory and register
    Load data from memory into register
    Store register data into memory
  Transfer control
    Unconditional jumps to/from procedures
    Conditional branches

## Slide 29: x86 Characteristics
Variable length instructions: 1-15 bytes
Can address memory directly in most instructions
Uses Little-Endian format

## Slide 30: Instruction Format
General format:
opcode operands
Opcode:
  Short mnemonic for instruction’s purpose
    movb,addl, etc.
Operands:
  Immediate, register, or memory
  Number of operands command-dependent
Example:
  movl %ebx, (%ecx)

## Slide 31: Machine Representation
Remember, each assembly instruction translated to a sequence of 1-15 bytes
First byte holds the binary representation of the opcode
Second byte specifies the addressing mode
  The type of operands (registers or register and memory)
  How to interpret the operands
Some instructions can be single-byte because operands and addressing mode are implicitly specified by the instruction
  E.g., pushl
other bytes
addressing mode byte
opcode byte