## Slide 1: Assembly Programming
Abhishek Bhattacharjee
Topics
  Introduction to Assembly Programming
    x86 assembly

## Slide 2: Programming Meets Hardware
High-Level Language Program
Assembly Language Program
Machine Language Program
movl $1, -8(%ebp)
movl $2, -12(%ebp)
movl -8(%ebp), %eax
movl %eax, -16(%ebp)
movl -12(%ebp), %eax
movl %eax, -8(%ebp)
movl -16(%ebp), %eax
movl %eax, -12(%ebp)
movl -16(%ebp), %eax
movl %eax, 12(%esp)
movl -12(%ebp), %eax
movl %eax, 8(%esp)
movl -8(%ebp), %eax
movl %eax, 4(%esp)
7f 45 4c 46 01 01 01
00 00 00 00 00 00 00
00 00 02 00 03 00 01
00 00 00 f0 82 04 08
34 00 00 00 c4 0c 00
00 00 00 00 00 34 00
#include <stdio.h>
int main() {
int x, y, temp;
x=1; y=2;
temp =x; x=y; y=temp;
printf("%d %d %d\n",x,y,temp);
}
ISA
Compiler
Assembler

## Slide 3: P6 Decoder/Interpreter

## Slide 4: Assembly Programmer’s View
Control
Logic
(OS code & data)
Object Code
Program Data
Addresses
Data
Instructions
Registers
ALU
CPU
Memory
Condition
Codes
PC

## Slide 5: Putting It All Together
ALU
Control
Logic
Registers
Program Counter (PC)
00101100
10001000
11111111
01010101
01010101
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
CPU
Condition Codes

## Slide 6: Putting It All Together
ALU
Control
Logic
Registers
Program Counter (PC)
00101100
10001000
11111111
01010101
01010101
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
CPU
Condition Codes
1

## Slide 7: Putting It All Together
ALU
Control
Logic
Registers
Program Counter (PC)
00101100
10001000
11111111
01010101
01010101
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
CPU
Condition Codes
1
1
10001000

## Slide 8: Putting It All Together
ALU
Control
Logic
Registers
Program Counter (PC)
00101100
10001000
11111111
01010101
01010101
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
CPU
Condition Codes
1
1
10001000
+
R0
R1
R0: x
R1: y

## Slide 9: Putting It All Together
ALU
Control
Logic
Registers
Program Counter (PC)
00101100
10001000
11111111
01010101
01010101
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
CPU
Condition Codes
1
1
10001000
+
R0
R1
x
y
R0: x
R1: y

## Slide 10: Putting It All Together
ALU
Control
Logic
Registers
Program Counter (PC)
00101100
10001000
11111111
01010101
01010101
11000001
00000000
11111001
11111000
00110000
00000000
00000000
00000000
11000011
00011001
00000000
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
Memory
Addresses
Storage
CPU
Condition Codes
2
1
10001000
+
R0
R1
x
y
z
R2: z
R0: x
R1: y
R2

## Slide 11: Assembly Characteristics
Primitive Operations
  Perform arithmetic function on register or memory data
  Transfer data between memory and register
    Load data from memory into register
    Store register data into memory
  Transfer control
    Unconditional jumps to/from procedures
    Conditional branches

## Slide 12: Instruction Format
General format:
opcode operands
Opcode:
  Short mnemonic for instruction’s purpose
    movb,addl, etc.
Operands:
  Immediate, register, or memory
  Number of operands command-dependent
Example:
  movl %ebx, (%ecx)

## Slide 13: Machine Representation
Remember, each assembly instruction translated to a sequence of 1-15 bytes
First byte holds the binary representation of the opcode
Second byte specifies the addressing mode
  The type of operands (registers or register and memory)
  How to interpret the operands
Some instructions can be single-byte because operands and addressing mode are implicitly specified by the instruction
  E.g., pushl
other bytes
addressing mode byte
opcode byte

## Slide 14: MOV instruction
Most common instruction is data transfer instruction
  mov S, D
    Copy value at S to D
Used to copy data from:
  Memory to register
  Register to memory
  Register to register
  Constant to register

## Slide 15: Data Formats
Byte: 8 bits
  E.g., char
Word: 16 bits (2 bytes)
  E.g., short int
Double Word: 32 bits ( 4 bytes)
  E.g., int, float
Quad Word: 64 bits (8 bytes)
  E.g., double
Instructions can operate on any data size
  movl, movw, movb
    Move double word, word, byte, respectively
  End character specifies what data size to be used

## Slide 16: x86 Registers
General purpose registers are 32 bit
  Although operations can access 8-bits or 16-bits portions
Originally categorized into two groups with different functionality
  Data registers (EAX, EBX, ECX, EDX)
    Holds operands
  Pointer and Index registers (EBP, ESP, EIP,ESI,EDI)
    Holds references to addresses as well as indexes
Now, the registers are mostly interchangeable
Segment registers
  Holds starting address of program segments
    CS, DS, SS, ES

## Slide 17: x86 Registers
EAX AX | AH | AL
ECX CX | CH | CL
EDX DX | DH | DL
EBX BX | BH | BL
ESP --Stack Pointer EBP --- Base register of current stack frame |  | 
ESI --- Source index for string operations |  | 
EDI --- Destination index for string operations |  | 
16 BITS
64 BITS
8 BITS

## Slide 18: Immediate Addressing
Operand is immediate
  Operand value is found immediately following the instruction
  $ in front of immediate operand
  E.g., movl $0x4040, %eax
movl %eax
4040
000f
00A1
00A2
memory
ADDR

## Slide 19: Direct Addressing
Address of operand is found immediately after the instruction
  Also known as direct addressing or absolute address
  movl %eax, 0x0000f
2009
eax
movl eax
0000f
2009
0x000f

## Slide 20: Register Mode Addressing
Use % to denote register
  E.g., %eax
Source operand: use value in specified register
Destination operand: use register as destination for value
Examples:
  movl %eax, %ebx
    Copy content of %eax to %ebx
  movl $0x4040, %eax  immediate addressing
    Copy 0x4040 to %eax
  movl %eax, 0x0000f  direct addressing
    Copy content of %eax to memory location 0x0000f

## Slide 21: Indirect Mode Addressing
Content of operand is an address
  Designated as parenthesis around operand
Offset can be specified as immediate mode
Examples:
  movl (%ebp), %eax
    Copy value from memory location whose address is in ebp into eax
  movl -4(%ebp), %eax
    Copy value from memory location whose address is -4 away from content of ebp into eax

## Slide 22: Indexed Mode Addressing
Add content of two registers to get address of operand
  movl (%eab, %esi), %eax
    Copy value at (address = eab + esi) into eax
  movl 8(%eab, %esi),%eax
    Copy value at (address = 8 + eab + esi) into eax
Useful for dealing with arrays
  If you need to walk through the elements of an array
  Use one register to hold base address, one to hold index
    E.g., implement C array access in a for loop

## Slide 23: Address Computation Examples
%edx
%ecx
0xf000
0x100
Expression | Computation | Address
0x8(%edx) | 0xf000 + 0x8 | 0xf008
(%edx,%ecx) | 0xf000 + 0x100 | 0xf100
(%edx,%ecx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%edx,2) | 2*0xf000 + 0x80 | 0x1e080

## Slide 24: movl Operand Combinations
  Cannot do memory-memory transfers with single instruction
movl
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Destination
movl $0x4,%eax
movl $-147,(%eax)
movl %eax,%edx
movl %eax,(%edx)
movl (%eax),%edx
C Analog
temp = 0x4;
*p = -147;
temp2 = temp1;
*p = temp;
temp = *p;

## Slide 25: Stack Operations
By convention, %esp is used to maintain a stack in memory
  Used to support C function calls
%esp contains the address of top of stack
Instructions to push (pop) content onto (off of) the stack
  pushl %eax
    esp = esp – 4
    Memory[esp] = eax
  popl %ebx
    ebx = Memory[esp]
    esp = esp + 4
Where does the stack start? We’ll discuss later

## Slide 26: Using Simple Addressing Modes
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
pushl %ebp
movl %esp,%ebp
pushl %ebx
movl 12(%ebp),%ecx
movl 8(%ebp),%edx
movl (%ecx),%eax
movl (%edx),%ebx
movl %eax,(%edx)
movl %ebx,(%ecx)
movl -4(%ebp),%ebx
movl %ebp,%esp
popl %ebp
ret
Body
Set
Up
Finish

## Slide 27: Understanding Swap
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
movl 12(%ebp),%ecx # ecx = yp
movl 8(%ebp),%edx # edx = xp
movl (%ecx),%eax # eax = *yp (t1)
movl (%edx),%ebx # ebx = *xp (t0)
movl %eax,(%edx) # *xp = eax
movl %ebx,(%ecx) # *yp = ebx
Stack
Register Variable
%ecx yp
%edx xp
%eax t1
%ebx t0
yp
xp
Rtn adr
Old %ebp
%ebp
0
4
8
12
Offset
•
•
•
Old %ebx
-4

## Slide 28: Understanding Swap
movl 12(%ebp),%ecx # ecx = yp
movl 8(%ebp),%edx # edx = xp
movl (%ecx),%eax # eax = *yp (t1)
movl (%edx),%ebx # ebx = *xp (t0)
movl %eax,(%edx) # *xp = eax
movl %ebx,(%ecx) # *yp = ebx
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x104

## Slide 29: Understanding Swap
movl 12(%ebp),%ecx # ecx = yp
movl 8(%ebp),%edx # edx = xp
movl (%ecx),%eax # eax = *yp (t1)
movl (%edx),%ebx # ebx = *xp (t0)
movl %eax,(%edx) # *xp = eax
movl %ebx,(%ecx) # *yp = ebx
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x120
0x104

## Slide 30: Understanding Swap
movl 12(%ebp),%ecx # ecx = yp
movl 8(%ebp),%edx # edx = xp
movl (%ecx),%eax # eax = *yp (t1)
movl (%edx),%ebx # ebx = *xp (t0)
movl %eax,(%edx) # *xp = eax
movl %ebx,(%ecx) # *yp = ebx
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x124
0x120
0x104

## Slide 31: Understanding Swap
movl 12(%ebp),%ecx # ecx = yp
movl 8(%ebp),%edx # edx = xp
movl (%ecx),%eax # eax = *yp (t1)
movl (%edx),%ebx # ebx = *xp (t0)
movl %eax,(%edx) # *xp = eax
movl %ebx,(%ecx) # *yp = ebx
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
456
0x124
0x120
0x104

## Slide 32: Understanding Swap
movl 12(%ebp),%ecx # ecx = yp
movl 8(%ebp),%edx # edx = xp
movl (%ecx),%eax # eax = *yp (t1)
movl (%edx),%ebx # ebx = *xp (t0)
movl %eax,(%edx) # *xp = eax
movl %ebx,(%ecx) # *yp = ebx
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
456
0x124
0x120
123
0x104

## Slide 33: Understanding Swap
movl 12(%ebp),%ecx # ecx = yp
movl 8(%ebp),%edx # edx = xp
movl (%ecx),%eax # eax = *yp (t1)
movl (%edx),%ebx # ebx = *xp (t0)
movl %eax,(%edx) # *xp = eax
movl %ebx,(%ecx) # *yp = ebx
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
456
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
456
0x124
0x120
123
0x104

## Slide 34: Understanding Swap
movl 12(%ebp),%ecx # ecx = yp
movl 8(%ebp),%edx # edx = xp
movl (%ecx),%eax # eax = *yp (t1)
movl (%edx),%ebx # ebx = *xp (t0)
movl %eax,(%edx) # *xp = eax
movl %ebx,(%ecx) # *yp = ebx
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
456
123
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
456
0x124
0x120
123
0x104

## Slide 35: Address Computation Instruction
leal: compute address using addressing mode without accessing memory
leal src, dest
  src is address mode expression
  Set dest to address specified by src
Use
  Computing address without doing memory reference
    E.g., translation of p = &x[i];
Example:
  leal 7(%edx, %edx, 4), %eax
    eax = 4*edx + edx + 7 = 5*edx + 7

## Slide 36: Some Arithmetic Operations
  Instruction Computation
  addl Src,Dest Dest = Dest + Src
  subl Src,Dest Dest = Dest - Src
  imull Src,Dest Dest = Dest * Src
  sall Src,Dest Dest = Dest << Src (left shift)
  sarl Src,Dest Dest = Dest >> Src (right shift)
  xorl Src,Dest Dest = Dest ^ Src
  andl Src,Dest Dest = Dest & Src
  orl Src,Dest Dest = Dest | Src

## Slide 37: Some Arithmetic Operations
  Instruction Computation
  incl Dest Dest = Dest + 1
  decl Dest Dest = Dest - 1
  negl Dest Dest = - Dest
  notl Dest Dest = ~ Dest